## Slide 1
WSQ COURSE SLIDES
Electrostatic Discharge (ESD) Control for Lab and Factory Engineers and Managers
TGS-2024051412
TSC: Electrostatic Discharge Control · ELE-OPR-4002-1.1
Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Trainer: Dr Alfred Ang
v3.1 · 20 August 2026

## Slide 2
MANDATORY
Digital Attendance (TRAQOM · SSG)
1
AM attendance
Scan the live QR code shown by the trainer.
2
PM attendance
Complete the required afternoon record.
3
Assessment attendance
Complete before sitting the assessment.
4
Use the live LMS
Do not reuse a screenshot or old QR code.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
1

## Slide 3
GENERAL TRAINER
About the Trainer
?
General Trainer
Complete before class
NAME ____________________________________________
TITLE / DESIGNATION ____________________________________________
QUALIFICATIONS ____________________________________________
AREAS OF EXPERTISE ____________________________________________
TRAINING & INDUSTRY EXPERIENCE ____________________________________________
CONTACT ____________________________________________
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
2

## Slide 4
NAMED TRAINER
About the Trainer
AA
Dr Alfred Ang
Lead Trainer · Tertiary Infotech Academy
NAME Dr Alfred Ang
TITLE / DESIGNATION Founder and principal trainer
QUALIFICATIONS Doctorate · engineering and digital transformation
AREAS OF EXPERTISE Technology, quality, process and AI-enabled work
TRAINING & INDUSTRY EXPERIENCE Adult learning and enterprise implementation
CONTACT enquiry@tertiaryinfotech.com
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
3

## Slide 5
LEARNER INTRODUCTION
Let’s know each other
1
Name and role
2
Lab or factory process you support
3
One ESD challenge you want to solve
4
One measurement or control item you already use
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
4

## Slide 6
CLASS AGREEMENT
Ground Rules
1
Participate
Ask, challenge and share evidence.
2
Respect
One conversation; disagree with ideas, not people.
3
Protect confidentiality
Use fictional scenarios; do not expose customer data.
4
Be punctual
Return from breaks on time.
5
Phones silent
Step out quietly for urgent calls.
6
Safety first
Stop any activity that conflicts with site electrical or process safety.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
5

## Slide 7
COURSE PORTAL
Login to LMS and Download Course Material
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
5
Log in at lms-tms.tertiaryinfotech.com with your registered email and the OTP sent to your inbox, then open this course to download the slides and Learner Guide.

## Slide 8
LESSON PLAN
Two-day course architecture
1
Day 1
ESD fundamentals, failure mechanisms and control implementation.
2
Day 2
Standards, measurement, audit, incident response and management control.
3
Assessment
1 h WA + 1 h Case Study; open book; submit on LMS.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
7

## Slide 9
COURSE OUTCOMES
Learning Outcomes
1
LO1
Apply control measures to manage ESD generation based on ESD principles.
2
LO2
Evaluate and recommend actions to improve ESD control effectiveness in accordance with ESD standards.
3
Evidence
Eight realistic activities build audit-ready outputs.
4
Transfer
Every activity mirrors lab/factory decisions.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
8

## Slide 10
ELECTROSTATIC DISCHARGE CONTROL · ELE-OPR-4002-1.1
TSC Knowledge and Abilities
1
K1
Introduction to ESD theory and principles, test models and ESD control items.
2
K2
Static control with respect to established ESD standards.
3
K3
Types of ESD instruments used for checks and measurements.
4
K4
Preventive measures to reduce the risk of ESD generation.
5
A1
Perform control measures to control the generation of ESD.
6
A2
Monitor the effectiveness of employed ESD control measures.
7
A3
Recommend follow-up actions to reduce the risk of ESD generation.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
9

## Slide 11
ADMIN
Briefing for Assessment
CANDIDATE CONDUCT
● Individual work; no discussion.
● Open book: course slides, Learner Guide and approved materials.
● Phones and other materials under the table.
● Use black/blue pen; no correction fluid.
INSTRUMENTS
● WA: 4 open-ended questions, K1–K4, 1 hour.
● Case Study: 2 open-ended tasks, A1–A3, 1 hour.
● Submit completed answers on the LMS.
● Reassessment and appeal rights apply.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
10

## Slide 12
ADMIN
Assessment and Funding
ELIGIBILITY
● Minimum 75% SSG digital attendance.
● Complete both assessment instruments.
● Competent outcome required for successful completion.
OUTCOME
● Assessment evidence must be your own work.
● Assessor feedback explains the decision.
● Appeal may be lodged through the published process.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
11

## Slide 13
ASSESSMENT · OPEN BOOK
Assessment Flow
1
TRAQOM digital attendance
▶
2
Assessment digital attendance
▶
3
Sit WA then Case Study
▶
4
Submit answers on the LMS
▶
5
Sign Assessment Summary Record
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
12

## Slide 14
HANDS-ON MATERIALS
Access the Course Activities
1
Open the course GitHub repository
▶
2
Choose Clone or Download ZIP
▶
3
Open the activities/ folder
▶
4
Start with the numbered README
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
13
Open the course activity repository

## Slide 15
REASONING CHECKPOINT 1 OF 3
How to reason about ESD exposure
1
Recognise the charge source, field and vulnerable item before selecting a control.
Detailed execution steps and evidence templates are in the Learner Guide and activity folder.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
14

## Slide 16
MODULE 1 · K1 · A1
Basics of ESD
Charge generation · discharge paths · HBM/MM/CDM · failure modes · business impact
01
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
15

## Slide 17
MODULE 1 · ESDA FUNDAMENTALS PART 1
A sudden charge transfer can damage a device without a visible spark or a felt shock.
Treat every unprotected ESDS item as vulnerable throughout handling, test, storage and service.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
16

## Slide 18
MODULE 1 · ESDA FUNDAMENTALS PART 1
The charge–field–discharge chain
1
Contact and separation create charge
▶
2
Charge remains on isolated conductors or insulators
▶
3
An electric field polarises nearby objects
▶
4
A conductive path forms
▶
5
Fast current damages a vulnerable device
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
17

## Slide 19
MODULE 1 · ESDA FUNDAMENTALS PART 1
Triboelectric charging
1
Material pair
Different electron affinities drive polarity and magnitude.
2
Contact area
More intimate contact can transfer more charge.
3
Separation
Speed and force affect charge generation.
4
Environment
Humidity and contamination change surface leakage.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
18

## Slide 20
MODULE 1 · ESDA FUNDAMENTALS PART 1
Conductors, dissipative materials and insulators
PRINCIPLE / USE
● Conductors redistribute charge quickly and can be grounded.
● Dissipative materials move charge in a controlled manner.
RISK / DECISION
● Insulators retain localised charge and cannot be neutralised by grounding alone.
● Low-charging, dissipative and shielding are different material functions.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
19

## Slide 21
MODULE 1 · ESDA FUNDAMENTALS PART 1
A metal tool, trolley or fixture can remain charged when it has no verified path to ground.
Bonding removes potential differences; grounding provides a controlled reference path.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
20

## Slide 22
MODULE 1 · ESDA FUNDAMENTALS PART 1
Electrostatic induction and polarisation
1
Charged object approaches
▶
2
Field redistributes charge in nearby conductor
▶
3
Temporary ground connection permits charge flow
▶
4
Ground is removed
▶
5
Object retains a net charge after the field leaves
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
21

## Slide 23
MODULE 1 · ANALOG DEVICES ESD GLOSSARY
Contact discharge versus air discharge
PRINCIPLE / USE
● Contact discharge: differently charged objects touch and charge transfers directly.
● Waveform depends on the source, path impedance and contact geometry.
RISK / DECISION
● Air discharge: a strong field ionises an air gap before contact.
● Visible sparks represent only a subset of damaging ESD events.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
22

## Slide 24
MODULE 1 · ESDA FUNDAMENTALS PART 1
What controls discharge severity?
1
Voltage difference
Stored potential is one risk indicator, not the whole event.
2
Capacitance
More stored charge can raise available energy.
3
Path impedance
Resistance and inductance shape peak current and rise time.
4
Device sensitivity
Pins, package and internal structures determine failure threshold.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
23

## Slide 25
MODULE 1 · ANALOG DEVICES ESD GLOSSARY
Human Body Model (HBM)
PRINCIPLE / USE
● Represents a charged person discharging through a device pin.
● Useful for component qualification and handling robustness.
RISK / DECISION
● A laboratory model—not a prediction of every factory event.
● Use supplier sensitivity data and the applicable controlled test method.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
24

## Slide 26
MODULE 1 · MODEL / PROTECTION VISUAL
HBM qualification uses a defined source network
Technical figure retained from source deck slide 39
1
Capacitance and series resistance shape the test pulse.
2
The network stresses a defined pin pair under a controlled method.
3
Qualification evidence does not predict every workplace event.
Use the current controlled standard and test method for execution.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
25

## Slide 27
MODULE 1 · ANALOG DEVICES ESD GLOSSARY
Machine Model (MM): legacy context
PRINCIPLE / USE
● Historically represented charged metal equipment with a low-impedance discharge.
● Appears in the legacy deck and some older literature.
RISK / DECISION
● Do not assume correlation with HBM or CDM.
● Use the test model and revision required by the current product/customer specification.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
26

## Slide 28
MODULE 1 · ESDA FUNDAMENTALS PART 1
Charged Device Model (CDM)
1
Device package becomes charged
▶
2
Device approaches grounded metal
▶
3
One pin makes first contact
▶
4
Very fast discharge leaves the device
▶
5
Local current density stresses internal structures
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
27

## Slide 29
MODULE 1 · MODEL / PROTECTION VISUAL
CDM tester: charge the device, then ground one pin
Technical figure retained from source deck slide 208
1
The package sits above a field plate during charging.
2
A grounded pogo pin initiates the very fast discharge.
3
Package, pin and current path influence local stress.
Use the current controlled standard and test method for execution.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
28

## Slide 30
MODULE 1 · ANALOG DEVICES ESD GLOSSARY
HBM, MM and CDM are not interchangeable
1
HBM
Charged person → device; handling-oriented component model.
2
MM
Legacy charged-machine representation; limited correlation.
3
CDM
Charged device → ground; very fast package-dependent event.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
29

## Slide 31
MODULE 1 · MODEL / PROTECTION VISUAL
Source and device determine the discharge path
Technical figure retained from source deck slide 32
1
A charged person may inject current through a pin or package path.
2
A charged device can discharge to grounded metal without human contact.
3
Select the model that matches the qualification question—not the most familiar acronym.
Use the current controlled standard and test method for execution.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
30

## Slide 32
MODULE 1 · ESDA FUNDAMENTALS PART 1
Catastrophic failure
1
Metal melt
Current density damages interconnects.
2
Junction breakdown
Semiconductor junction no longer meets specification.
3
Oxide rupture
Thin dielectric is punctured.
4
Immediate detection
Device may fail functional or parametric test.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
31

## Slide 33
MODULE 1 · ESDA FUNDAMENTALS PART 1; TOSHIBA ESD FAQ
Physical defect signatures
1
Gate oxide rupture
A local dielectric puncture can create leakage, a short or loss of control.
2
Junction damage
High current density can produce leakage, spiking or a shorted junction.
3
Metallisation damage
Local heating can melt, open or bridge an interconnect.
4
Passivation and edge damage
Surface or edge breakdown can shift parameters and weaken long-term margin.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
32

## Slide 34
MODULE 1 · ESDA FUNDAMENTALS PART 1; ANALOG DEVICES
Latent and cumulative degradation
PRINCIPLE / USE
● A degraded device may still pass initial functional test.
● Leakage or margins can shift after an event.
RISK / DECISION
● The latent-failure concept is debated; evidence must distinguish ESD from other overstress causes.
● Repeated mishandling can cumulatively degrade parameters.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
33

## Slide 35
MODULE 1 · ESDA FUNDAMENTALS PART 1
ESD versus electrical overstress (EOS)
PRINCIPLE / USE
● ESD: rapid electrostatic charge transfer, usually short duration and fast rise time.
● Evidence includes handling history, field sources and microscopic damage pattern.
RISK / DECISION
● EOS: broader excessive electrical energy exposure from power, wiring or transients.
● Do not label every burnt part as ESD without a disciplined failure analysis.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
34

## Slide 36
MODULE 1 · TOSHIBA ESD FAQ; ANALOG DEVICES ESD GLOSSARY
Device-level protection techniques
1
Steering diodes
Route pin current toward supply rails.
2
Clamp structures
Turn on during a transient to limit internal voltage.
3
Series impedance
Restrict current and reduce stress entering the core.
4
Layout discipline
Short, low-inductance paths and adequate spacing make protection effective.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
35

## Slide 37
MODULE 1 · MODEL / PROTECTION VISUAL
Protection structures divert current from the core
Technical figure retained from source deck slide 87
1
Rail-steering structures provide a lower-stress current path.
2
Clamp and layout performance depend on the complete transient path.
3
External handling controls remain necessary for qualified devices.
Use the current controlled standard and test method for execution.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
36

## Slide 38
MODULE 1 · ESDA FUNDAMENTALS PART 1
Where exposure occurs
1
Component manufacture
▶
2
Incoming inspection
▶
3
Assembly and test
▶
4
Packaging and logistics
▶
5
Installation and field service
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
37

## Slide 39
MODULE 1 · ESDA FUNDAMENTALS PART 1
Which devices may be sensitive?
1
Semiconductors
ICs, MOSFETs, diodes and precision analog parts.
2
Assemblies
Populated PCBs and hybrid circuits.
3
Sensors
Optoelectronic, microwave, piezoelectric and recording-head devices.
4
Supplier data
Actual sensitivity comes from product qualification information.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
38

## Slide 40
MODULE 1 · ESDA FUNDAMENTALS PART 1
Economic impact pathway
1
Undetected ESD exposure
▶
2
Yield loss or rework
▶
3
Escapes and field returns
▶
4
Warranty and investigation cost
▶
5
Customer trust and regulatory impact
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
39

## Slide 41
MODULE 1 · ESDA FUNDAMENTALS PART 1; ANALOG DEVICES
The reliability escape chain
1
Uncontrolled electrostatic exposure
▶
2
Physical damage or parametric shift
▶
3
Test misses or misclassifies the defect
▶
4
Degraded unit escapes
▶
5
Intermittent field failure or return
▶
6
Evidence feeds prevention and design improvement
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
40

## Slide 42
MODULE 1 · ESDA FUNDAMENTALS PART 1
Risk-based prioritisation
1
Sensitivity
Lowest credible device withstand level.
2
Exposure
People, motion, insulators, automation and transport.
3
Detectability
Whether damage is caught before shipment.
4
Consequence
Safety, quality, cost, customer and downtime impact.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
41

## Slide 43
Lunch Break
45 minutes
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
42

## Slide 44
ACTIVITY 01 · K1 · A1
Static Hazard Hunt at NovaSense Incoming Inspection
NovaSense receives MEMS sensor trays beside a label printer, stretch-wrap station and wheeled inspection trolley. Failure returns increased after a layout change, but no one has mapped charge-generation and induction risks.
MISSION
Identify credible charge sources, exposed ESDS items, isolated conductors and field-coupling paths, then prioritise controls.
Roles: ESD engineer · incoming-inspection supervisor · quality observer
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
43

## Slide 45
ACTIVITY 01
Scenario questions
DISCUSS / DECIDE
● Which hazard could damage a device without a visible spark?
● Which metal object could remain charged despite being conductive?
● What evidence would distinguish induction risk from direct contact?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
44

## Slide 46
ACTIVITY 01 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Annotated hazard map
● Risk-prioritisation worksheet
● Three-control proposal
● Peer-review note
ACCEPTANCE CRITERIA
✓ At least eight credible hazards are identified
✓ Both direct and field-induced pathways are shown
✓ Top risks have evidence-based ratings
✓ Controls follow the ESD control hierarchy
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
45

## Slide 47
ACTIVITY 02 · K1 · A1
Medical Microchip Failure Triage: ESD, EOS or Process Defect?
A medical-device ASIC passes wafer test but shows intermittent leakage after final assembly. A handler alarm occurred during the lot, yet the power-supply log also shows a transient. Management wants a defensible triage before quarantined product is released.
MISSION
Build an evidence-based hypothesis that separates HBM/CDM exposure, EOS and non-electrical process causes.
Roles: reliability engineer · failure-analysis lead · production manager
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
46

## Slide 48
ACTIVITY 02
Scenario questions
DISCUSS / DECIDE
● Why is a monitor alarm not proof that this device was damaged by ESD?
● Which facts make CDM plausible?
● What would make the latent-failure claim weak?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
47

## Slide 49
ACTIVITY 02 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Chronology
● Hypothesis matrix
● Containment plan
● Decision-gate briefing
ACCEPTANCE CRITERIA
✓ ESD, EOS and process alternatives remain explicit
✓ Evidence needed for each hypothesis is stated
✓ Containment protects product and evidence
✓ Conclusions use calibrated language
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
48

## Slide 50
RETRIEVAL PRACTICE
Module 1 recap
1
Risk
Charge generation · discharge paths · HBM/MM/CDM · failure modes · business impact
2
Knowledge
K1 · A1
3
Evidence
Explain the decision and retain traceable records.
4
Next
Carry the controls into the following module.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
49

## Slide 51
MODULE 2 · K1 · K3 · K4 · A1
ESD Control Principles, Equipment and Practices
EPA design · grounding and bonding · personnel controls · ionisation · packaging · maintenance
02
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
50

## Slide 52
MODULE 2 · ESDA FUNDAMENTALS PART 1
The ESD control hierarchy
1
Identify ESDS items and process limits
▶
2
Remove unnecessary charge generators
▶
3
Ground and bond conductors
▶
4
Neutralise essential insulators
▶
5
Shield during storage and transport
▶
6
Verify and improve
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
51

## Slide 53
MODULE 2 · ESDA FUNDAMENTALS PART 1
Electrostatic Protected Area (EPA)
1
Boundary
A defined area with controlled entry and clear visual identification.
2
Common point
A known reference for compatible grounding and bonding.
3
Approved items
Only qualified materials, tools and equipment inside.
4
Behaviour
Handling rules, training and compliance verification are enforced.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
52

## Slide 54
MODULE 2 · OPERATING CONTEXT
An EPA is a controlled system—not a bench accessory
1
Defined boundary and authorised materials
2
Equipotential paths for people, bench and fixtures
3
Handling discipline plus verification evidence
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
53

## Slide 55
MODULE 2 · ESDA FUNDAMENTALS PART 1
Grounding versus bonding
PRINCIPLE / USE
● Grounding connects a conductor to a verified reference.
● Personnel and equipment paths must be compatible with safety requirements.
RISK / DECISION
● Bonding connects conductors so they remain at substantially the same potential.
● Bond isolated metal objects even when they are not intentionally energised.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
54

## Slide 56
MODULE 2 · ESDA FUNDAMENTALS PART 1
Common point ground architecture
1
Facilities/equipment ground verified
▶
2
EPA common point established
▶
3
Mat and fixtures bonded
▶
4
Personnel grounding connected
▶
5
Continuity monitored and recorded
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
55

## Slide 57
MODULE 2 · ESDA FUNDAMENTALS PART 1
Personnel grounding choices
1
Seated work
Wrist strap with tested cord and verified connection.
2
Standing/mobile
Foot grounders or qualified footwear/flooring system.
3
Continuous monitoring
Real-time alarm when the selected path leaves limits.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
56

## Slide 58
MODULE 2 · ESDA FUNDAMENTALS PART 1
Wrist-strap control loop
1
Inspect band and cord
▶
2
Test before use
▶
3
Connect to approved point
▶
4
Maintain skin contact
▶
5
Respond immediately to alarm/failure
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
57

## Slide 59
MODULE 2 · ESDA FUNDAMENTALS PART 1
Footwear and flooring as a system
PRINCIPLE / USE
● Foot grounders/ESD footwear provide the personnel interface.
● Correct wear and both-foot coverage matter.
RISK / DECISION
● Qualified flooring completes the path.
● Contamination, wax, humidity and wear can change performance.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
58

## Slide 60
MODULE 2 · ESDA FUNDAMENTALS PART 1
Worksurface and tool control
1
Dissipative mat
Provides controlled charge decay and a defined work zone.
2
Grounded fixtures
Prevents isolated conductive metal.
3
ESD-safe tools
Tweezers, brushes and dispensers selected for the process.
4
Housekeeping
Cleaners and residues must not defeat electrical properties.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
59

## Slide 61
MODULE 2 · ESDA FUNDAMENTALS PART 1
Essential insulators
1
Identify the process need
▶
2
Measure field at the actual use distance
▶
3
Increase separation where possible
▶
4
Apply ionisation or shielding
▶
5
Verify after changes
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
60

## Slide 62
MODULE 2 · ESDA FUNDAMENTALS PART 1
Ionisation
PRINCIPLE / USE
● Balanced positive and negative ions neutralise charges on insulators and isolated conductors.
● Use where grounding is ineffective or impossible.
RISK / DECISION
● Verify offset/balance and decay performance at the work location.
● Airflow, distance, contamination and emitter maintenance affect results.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
61

## Slide 63
MODULE 2 · ESDA FUNDAMENTALS PART 1
Electrostatic field shielding
1
Conductive enclosure
Redistributes external charge and protects contents when closed.
2
Shielding bag
Provides a protective envelope for transport outside the EPA.
3
Continuity
Seams, closures and openings determine actual performance.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
62

## Slide 64
MODULE 2 · ESDA FUNDAMENTALS PART 1
Packaging functions are different
1
Low charging
Limits triboelectric generation during contact/separation.
2
Dissipative
Moves charge in a controlled way.
3
Conductive
Rapidly redistributes charge; may need grounding.
4
Shielding
Attenuates discharge current and electrostatic fields around contents.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
63

## Slide 65
MODULE 2 · ANALOG DEVICES; ELECTROSTATIC-SENSITIVE DEVICE OVERVIEW
Handling ESDS items
1
Confirm EPA readiness
▶
2
Ground the handler
▶
3
Open shielding package inside EPA
▶
4
Handle by body/edges
▶
5
Return to protective packaging before leaving
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
64

## Slide 66
MODULE 2 · OPERATING CONTEXT
Safe handling keeps product inside a verified protection envelope
1
Ground the complete person-to-reference path
2
Hold assemblies by edges and avoid terminals
3
Open and close shielding packaging only in the controlled area
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
65

## Slide 67
MODULE 2 · ESDA FUNDAMENTALS PART 1
Garments, gloves and finger cots
PRINCIPLE / USE
● Garments control charge from clothing and help contain personal items.
● Select design and grounding method for the process.
RISK / DECISION
● Gloves/finger cots may support contamination control but are not automatically ESD-safe.
● Qualification and correct use are required.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
66

## Slide 68
MODULE 2 · ESDA FUNDAMENTALS PART 1
Carts, racks and material movement
1
Conductive wheels
Maintain the intended path only when floor contact is suitable.
2
No loose insulators
Remove ordinary plastic wrap and foam near exposed ESDS items.
3
Covered transport
Use closed qualified containers outside EPA boundaries.
4
Route control
Avoid high-charging areas and unmanaged handoffs.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
67

## Slide 69
MODULE 2 · ESDA FUNDAMENTALS PART 1
Maintenance is part of control
1
Define owner and interval
▶
2
Inspect and clean
▶
3
Test with calibrated equipment
▶
4
Record result and disposition
▶
5
Trend failures and revise interval
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
68

## Slide 70
MODULE 2 · ESDA FUNDAMENTALS PART 1
Common failure patterns
1
Disconnected strap
Cord attached to an unverified point or worn over clothing.
2
Open bag
Shielding package left open or folded incorrectly.
3
Insulator creep
Tape, foam, trays or paperwork introduced without review.
4
Bad response
Alarm bypassed, failed tester ignored or record completed retrospectively.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
69

## Slide 71
MODULE 2 · ESDA FUNDAMENTALS PART 1
Supervisor’s EPA readiness review
1
People
Training current; grounding tested; behaviour observed.
2
Place
Boundary, common point, floor, mat and ioniser verified.
3
Product
Sensitivity known; packaging and process controls matched.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
70

## Slide 72
ACTIVITY 03 · K3 · K4 · A1
Design and Commission an EPA for Orion Optics
Orion Optics is moving laser-diode assembly into a small shared lab. The proposed bench has a mat and wrist strap but no documented boundary, common point, insulator policy or readiness test.
MISSION
Design an EPA that controls people, place, product and process, then define commissioning evidence.
Roles: ESD engineer · facilities engineer · lab manager
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
71

## Slide 73
ACTIVITY 03
Scenario questions
DISCUSS / DECIDE
● What makes the area an EPA rather than simply a bench with a mat?
● Which item cannot be made safe by grounding alone?
● What evidence authorises production start?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
72

## Slide 74
ACTIVITY 03 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● EPA layout
● Grounding/bonding diagram
● Insulator-control register
● Commissioning plan and readiness certificate
ACCEPTANCE CRITERIA
✓ Boundary and product flow are unambiguous
✓ All conductors have a resolved status
✓ Essential insulators have controls
✓ Commissioning includes method, limit, owner and response
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
73

## Slide 75
ACTIVITY 04 · K3 · K4 · A1
Select Controls for the Aster Robotics Handling Cell
A robot transfers packaged ICs from plastic tubes to a grounded nest. Operators also perform manual rework. The team proposes more wrist straps, but field readings near the tube exit remain high.
MISSION
Match grounding, ionisation, shielding, handling and monitoring controls to both human and automated exposure pathways.
Roles: automation engineer · ESD specialist · maintenance supervisor
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
74

## Slide 76
ACTIVITY 04
Scenario questions
DISCUSS / DECIDE
● Why will adding wrist straps not solve the tube-exit field?
● Which controls address CDM risk?
● What should happen when an ioniser check fails?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
75

## Slide 77
ACTIVITY 04 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Exposure-path map
● Control-selection matrix
● Monitoring/stop-condition plan
● Maintenance plan
ACCEPTANCE CRITERIA
✓ Controls cover human and automated pathways
✓ Insulators are addressed by an appropriate method
✓ Monitoring has explicit response actions
✓ Residual risk is stated
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
76

## Slide 78
RETRIEVAL PRACTICE
Module 2 recap
1
Risk
EPA design · grounding and bonding · personnel controls · ionisation · packaging · maintenance
2
Knowledge
K1 · K3 · K4 · A1
3
Evidence
Explain the decision and retain traceable records.
4
Next
Carry the controls into the following module.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
77

## Slide 79
Day 1 Complete
Return on time for Day 2 digital attendance
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
78

## Slide 80
MODULE 3 · K2 · K3 · A2 · A3
ESD Standards, Testing and Auditing
Control programme structure · measurements · compliance verification · evidence · performance metrics
03
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
79

## Slide 81
MODULE 3 · ESDA FUNDAMENTALS PART 1
ANSI/ESD S20.20-2021 and IEC 61340-5-1:2024 structure organisational controls for protecting ESDS items.
Use the current controlled copy, customer requirements and product sensitivity data for exact limits and methods.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
80

## Slide 82
MODULE 3 · EOS/ESD ASSOCIATION; IEC 61340-5-1:2024
The standards stack has distinct purposes
1
Programme requirements
ANSI/ESD S20.20-2021 or IEC 61340-5-1:2024 defines the control-programme framework.
2
Methods and verification
Referenced test methods and verification guidance define how control items are qualified and checked.
3
Site and customer controls
The approved control plan tailors product sensitivity, process risk, limits, frequency, records and response.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
81

## Slide 83
MODULE 3 · EOS/ESD ASSOCIATION
Control programme architecture
1
Scope and responsibilities
▶
2
Technical requirements
▶
3
Product qualification
▶
4
Compliance verification
▶
5
Records, corrective action and management review
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
82

## Slide 84
MODULE 3 · ESDA FUNDAMENTALS PART 1
Product qualification versus compliance verification
PRINCIPLE / USE
● Qualification demonstrates that an ESD control item/type is capable of meeting specified requirements.
● Evidence may include supplier data or internal testing.
RISK / DECISION
● Compliance verification checks that installed controls remain effective in routine use.
● It uses defined methods, frequencies, limits and response actions.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
83

## Slide 85
MODULE 3 · ESDA FUNDAMENTALS PART 1
Instrument-to-risk map
1
Resistance meter
Worksurfaces, floors, garments, packaging and ground paths.
2
Personnel tester
Wrist straps, footwear and person/footwear/floor systems.
3
Field meter
Electrostatic field and charged-object screening.
4
Charge plate monitor
Ioniser decay and offset/balance performance.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
84

## Slide 86
MODULE 3 · ESDA FUNDAMENTALS PART 1
Measurement discipline
1
Define method and limit
▶
2
Confirm calibration/status
▶
3
Condition sample/environment
▶
4
Measure at specified points
▶
5
Record result and uncertainty/context
▶
6
Act on failure
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
85

## Slide 87
MODULE 3 · OPERATING CONTEXT
Verification turns a control claim into traceable evidence
1
Use the specified instrument, electrodes and method
2
Record environment, location, units and first-pass result
3
Contain and investigate failures before accepting a retest
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
86

## Slide 88
MODULE 3 · ESDA FUNDAMENTALS PART 1
Wrist strap and footwear checks
PRINCIPLE / USE
● Daily/user checks screen the assembled personal grounding path before work.
● Failure requires immediate stop, retest and disposition.
RISK / DECISION
● Periodic technical checks verify components, testers and flooring systems.
● Trend repeated failures by user, device, location and shift.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
87

## Slide 89
MODULE 3 · ESDA FUNDAMENTALS PART 1
Surface and point-to-ground resistance
1
Point-to-point
Characterises the path across a surface/material.
2
Point-to-ground
Characterises the installed path to the designated ground.
3
Context
Electrodes, voltage, dwell, humidity and cleanliness influence the reading.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
88

## Slide 90
MODULE 3 · ESDA FUNDAMENTALS PART 1
Ioniser performance checks
1
Inspect placement and airflow
▶
2
Warm up per procedure
▶
3
Measure positive/negative decay
▶
4
Measure offset/balance
▶
5
Clean or adjust
▶
6
Repeat and record
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
89

## Slide 91
MODULE 3 · ESDA FUNDAMENTALS PART 1
Audit evidence pyramid
1
Observe
Actual behaviour at the workstation.
2
Measure
Current test results from calibrated instruments.
3
Interview
Personnel can explain risk and response.
4
Records
Training, qualification, maintenance, failures and CAPA are traceable.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
90

## Slide 92
MODULE 3 · ESDA FUNDAMENTALS PART 1
Risk-based audit sampling
PRINCIPLE / USE
● Increase attention where products are most sensitive, exposure is high or process changes are recent.
● Sample across shifts, people and workstations.
RISK / DECISION
● Do not let a checklist replace observation and measurement.
● A single passing sample does not prove the entire system.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
91

## Slide 93
MODULE 3 · ESDA FUNDAMENTALS PART 1
Nonconformity grading
1
Critical
Immediate product/safety exposure; contain and escalate.
2
Major
Systemic or repeated breakdown; formal CAPA and verification.
3
Minor/observation
Local weakness or improvement opportunity; track proportionately.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
92

## Slide 94
MODULE 3 · ESDA FUNDAMENTALS PART 1
Corrective-action loop
1
Contain affected product/process
▶
2
Define problem with evidence
▶
3
Analyse root and contributing causes
▶
4
Implement corrective/preventive actions
▶
5
Verify effectiveness
▶
6
Standardise and close
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
93

## Slide 95
MODULE 3 · ESDA FUNDAMENTALS PART 1
Useful ESD performance metrics
1
Leading
Test completion, first-pass pass rate, overdue calibration, training currency.
2
Process
EPA audit score, insulator findings, alarm response time.
3
Lagging
ESD-attributed escapes, scrap, rework and field returns.
4
Learning
Repeat causes, CAPA recurrence and time-to-effective closure.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
94

## Slide 96
MODULE 3 · ESDA FUNDAMENTALS PART 1
Management review questions
1
Effective?
Are controls reducing exposure and failures?
2
Adequate?
Do changes in products/processes require new controls?
3
Sustained?
Are verification, training and CAPA completed on time?
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
95

## Slide 97
ACTIVITY 05 · K2 · K3 · A2
Execute a Compliance Verification Round
Meridian Electronics has four EPAs on two shifts. Recent records show perfect results but several tester failures were repaired without documented product disposition. You must execute a verification round using a simulated data pack.
MISSION
Plan, execute and record traceable checks for personnel grounding, resistance, electrostatic field and ioniser performance.
Roles: ESD auditor · area owner · instrument custodian
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
96

## Slide 98
ACTIVITY 05
Scenario questions
DISCUSS / DECIDE
● Why is a retest pass insufficient without investigating the first failure?
● Which contextual data makes a resistance reading defensible?
● Where should ioniser performance be checked?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
97

## Slide 99
ACTIVITY 05 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Completed measurement log
● Failure/disposition records
● Metric calculation
● Signed evidence package
ACCEPTANCE CRITERIA
✓ Every result includes method, units and conditions
✓ Instrument status is verified
✓ First-pass failures remain visible
✓ Product impact and response are documented
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
98

## Slide 100
ACTIVITY 06 · K2 · A2 · A3
Standards-Based EPA Audit at Helix Assembly
Helix Assembly claims alignment to ANSI/ESD S20.20 and IEC 61340-5-1. A new customer requests evidence that controls are implemented, verified and improved—not merely purchased.
MISSION
Conduct a risk-based audit using observation, measurement, interview and records, then issue graded findings and corrective-action requests.
Roles: lead auditor · ESD programme coordinator · customer observer
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
99

## Slide 101
ACTIVITY 06
Scenario questions
DISCUSS / DECIDE
● What evidence shows a control is sustained rather than merely installed?
● Why must the exact controlled standard govern numerical limits?
● What makes a finding actionable?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
100

## Slide 102
ACTIVITY 06 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Audit plan
● Completed checklist
● Evidence register
● Graded findings and follow-up plan
ACCEPTANCE CRITERIA
✓ Sampling is risk-based
✓ Findings cite objective evidence
✓ Critical exposure triggers containment
✓ Follow-up tests effectiveness, not only completion
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
101

## Slide 103
RETRIEVAL PRACTICE
Module 3 recap
1
Risk
Control programme structure · measurements · compliance verification · evidence · performance metrics
2
Knowledge
K2 · K3 · A2 · A3
3
Evidence
Explain the decision and retain traceable records.
4
Next
Carry the controls into the following module.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
102

## Slide 104
Afternoon Break
10 minutes
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
103

## Slide 105
MODULE 4 · K4 · A2 · A3
Training, Awareness and Incident Improvement
Competence · behaviour · reporting · root-cause analysis · CAPA · management ownership
04
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
104

## Slide 106
MODULE 4 · ESDA FUNDAMENTALS PART 1
Competence is role-specific
1
Operators
Recognise ESDS items, enter EPA correctly and handle/pack safely.
2
Technicians
Set up, test, troubleshoot and maintain controls.
3
Engineers
Define limits, qualify controls and investigate events.
4
Managers
Provide resources, review metrics and remove systemic barriers.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
105

## Slide 107
MODULE 4 · ESDA FUNDAMENTALS PART 1
From awareness to reliable behaviour
1
Explain the invisible risk
▶
2
Demonstrate the correct method
▶
3
Practise with feedback
▶
4
Observe on the job
▶
5
Reinforce and requalify
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
106

## Slide 108
MODULE 4 · ESDA FUNDAMENTALS PART 1
ESD champions and supervision
1
Coach
Give immediate, specific feedback at the workstation.
2
Escalate
Stop unsafe handling and trigger containment when required.
3
Learn
Share incident lessons without normalising blame.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
107

## Slide 109
MODULE 4 · ESDA FUNDAMENTALS PART 1
Recognising a possible ESD incident
1
Product symptom
Sudden failure, parametric shift, intermittent behaviour or unexplained fallout.
2
Control signal
Monitor alarm, failed tester, ioniser drift or broken ground path.
3
Exposure clue
Unprotected handling, ordinary plastic, low humidity or process change.
4
Caution
Symptoms are not proof; preserve evidence for diagnosis.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
108

## Slide 110
MODULE 4 · ESDA FUNDAMENTALS PART 1
Immediate response
1
Stop and protect the process
▶
2
Segregate potentially affected product
▶
3
Preserve settings, logs and samples
▶
4
Notify defined roles
▶
5
Begin evidence-based triage
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
109

## Slide 111
MODULE 4 · ESDA FUNDAMENTALS PART 1
Incident evidence set
1
What/where/when
Product, lot, station, timestamp and sequence.
2
Environment
Humidity, temperature, nearby motion and insulators.
3
Controls
Tester logs, monitor alarms, grounding and ioniser status.
4
People/process
Who handled it, procedure used and recent changes.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
110

## Slide 112
MODULE 4 · OPERATING CONTEXT
Incident analysis protects both product and evidence
1
Preserve suspect parts, logs and workstation state
2
Separate ESD hypotheses from EOS and process alternatives
3
Convert findings into CAPA with an effectiveness check
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
111

## Slide 113
MODULE 4 · ESDA FUNDAMENTALS PART 1
Root-cause analysis without blame
PRINCIPLE / USE
● Ask why the system allowed exposure: design, maintenance, method, material, measurement or management.
● Distinguish root, contributing and detection causes.
RISK / DECISION
● Avoid stopping at 'operator error'.
● A repeated behaviour usually reflects unclear standards, weak design, workload or ineffective supervision.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
112

## Slide 114
MODULE 4 · ESDA FUNDAMENTALS PART 1
Selecting corrective actions
1
Remove generator/exposure
▶
2
Engineer a reliable ground or enclosure
▶
3
Add detection/monitoring
▶
4
Standardise work and response
▶
5
Train and verify competence
▶
6
Measure sustained effectiveness
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
113

## Slide 115
MODULE 4 · ESDA FUNDAMENTALS PART 1
Communicating ESD risk
1
Frontline
Show the exact handling risk and the stop-work response.
2
Engineering
Use measurements, failure evidence and process capability.
3
Management
Translate risk into yield, customer, compliance and continuity impact.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
114

## Slide 116
MODULE 4 · ESDA FUNDAMENTALS PART 1
A sustainable ESD culture
1
Visible ownership
Named programme coordinator and local owners.
2
Just reporting
Near misses and failures can be reported without concealment.
3
Closed loop
Findings become actions, verified changes and updated standards.
4
Learning cadence
Metrics, incidents and changes are reviewed regularly.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
115

## Slide 117
MODULE 4 · ESDA FUNDAMENTALS PART 1
Competency certification
PRINCIPLE / USE
● Internal authorisation should match the tasks a person performs.
● Use knowledge, demonstration and observed-work evidence.
RISK / DECISION
● External credentials may support development but do not replace site-specific qualification.
● Reassess after major changes, lapse or repeated nonconformance.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
116

## Slide 118
ACTIVITY 07 · K4 · A2 · A3
Investigate the PulseMed ESD Incident
PulseMed sees intermittent failures in a safety-relevant control board after a temporary operator used ordinary bubble wrap near final test. A monitor alarm was acknowledged but production continued for 47 minutes.
MISSION
Contain risk, preserve evidence, identify system causes and produce a verified CAPA plan.
Roles: incident lead · production manager · quality/reliability representative
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
117

## Slide 119
ACTIVITY 07
Scenario questions
DISCUSS / DECIDE
● Which system weakness allowed the alarm to be ignored?
● What evidence must be preserved before resetting the workstation?
● How will you prove the CAPA was effective?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
118

## Slide 120
ACTIVITY 07 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● Containment record
● Timeline and causal analysis
● CAPA plan
● Effectiveness-verification plan
ACCEPTANCE CRITERIA
✓ Exposure window and product scope are defined
✓ Causes extend beyond individual blame
✓ Actions address root and detection causes
✓ Effectiveness has measurable evidence
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
119

## Slide 121
ACTIVITY 08 · K1–K4 · A1–A3
Management Capstone: Build the Apex ESD Control Plan
Apex Microsystems is opening a mixed lab/factory line for sensitive industrial controllers. Management needs an auditable ESD control plan before customer qualification, covering controls, verification, competence, incidents and improvement.
MISSION
Integrate the complete course into a management-ready ESD control plan and defend it under assessment-style questioning.
Roles: ESD programme manager · operations manager · quality manager · customer assessor
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
120

## Slide 122
ACTIVITY 08
Scenario questions
DISCUSS / DECIDE
● How does the plan demonstrate A1, A2 and A3?
● Which records prove the control programme remains effective?
● What management decision is triggered by deteriorating leading indicators?
QUALITY OF REASONING
● Work from the evidence provided.
● State assumptions and missing evidence.
● Use current controlled limits and methods.
● Challenge the first explanation before concluding.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
121

## Slide 123
ACTIVITY 08 · VERIFY
Evidence and acceptance gate
EVIDENCE TO SUBMIT
● ESD control plan
● Qualification and verification matrices
● Competency matrix
● Metrics dashboard and 90-day roadmap
ACCEPTANCE CRITERIA
✓ All K and A criteria are traceable
✓ Controls have owners and evidence
✓ Failure response and CAPA are closed-loop
✓ Plan uses current controlled standards for exact requirements
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
122

## Slide 124
RETRIEVAL PRACTICE
Module 4 recap
1
Risk
Competence · behaviour · reporting · root-cause analysis · CAPA · management ownership
2
Knowledge
K4 · A2 · A3
3
Evidence
Explain the decision and retain traceable records.
4
Next
Carry the controls into the following module.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
123

## Slide 125
COURSE SUMMARY
What You Achieved
1
Recognise
Explain charge generation, induction, discharge models and damage.
2
Control
Design an EPA and select grounding, ionisation, shielding and packaging.
3
Verify
Choose instruments, evaluate records and audit programme effectiveness.
4
Improve
Investigate incidents, recommend CAPA and manage competence.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
124

## Slide 126
LMS
Courseware and Assessment on the LMS
1
Open the LMS portal
▶
2
Select this course record
▶
3
Download current courseware
▶
4
Complete WA and Case Study
▶
5
Upload completed answers
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
125
Open the LMS portal

## Slide 127
END-OF-COURSE REMINDER
Assessment
WA
● Written Assessment (SAQ): 1 hour.
● Four open-ended questions covering K1–K4.
CASE STUDY
● Case Study (CS): 1 hour.
● Two open-ended tasks covering A1–A3.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
126

## Slide 128
ASSESSMENT · OPEN BOOK
Assessment Flow · Final Reminder
1
TRAQOM digital attendance
▶
2
Assessment digital attendance
▶
3
Sit WA then Case Study
▶
4
Submit answers on the LMS
▶
5
Sign Assessment Summary Record
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
127

## Slide 129
SSG · ASSESSMENT
Digital Attendance (Mandatory)
1
TRAQOM
Scan the live assessment attendance QR code.
2
Verify
Confirm successful submission before assessment.
3
Privacy
Use your own details and device.
4
Support
Ask the trainer if the live code does not open.
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
128

## Slide 130
THANK YOU
ESD control is a system of engineered paths, disciplined behaviour and verified evidence.
Thank you · enquiry@tertiaryinfotech.com · +65 6100 0613
Electrostatic-Discharge-ESD-Control · TGS-2024051412
© Tertiary Infotech Academy Pte Ltd
129